## Slide 1: The role of buildings in Climate Change Adaptation
Buildings in the geospatial domain
Danny Vandenbroucke
KU Leuven (SADL)

## Slide 2: Learning Objectives
To identify different types of buildings and explain their variability
To understand and discuss how buildings can be represented in a geospatial context
To recognize and explain the most important EU initiatives related to buildings
To understand and discuss the potential role of buildings in the context of climate change challenges

## Slide 3: Structure of the lecture
Buildings and the urban fabric
Modelling buildings as geospatial objects
Buildings in important European initiatives
The role of buildings in CCA & CCM
Conclusions

## Slide 4: Structure of the lecture
Buildings and the urban fabric
Modelling buildings as geospatial objects
Buildings in important European initiatives
The role of buildings in CCA & CCM
Conclusions

## Slide 5: Buildings are everywhere …
… consist of different parts
Roof
Roof
Interior
Facade

## Slide 6: They are of different types …
… related to different functions
School
House
Office
Factory
Factory
Sports hall

## Slide 7: They are of different size …
… and form
Skyscrapers
Tiny house
Old house
Special shapes
Modern house

## Slide 8: Houses are not isolated …
… they have connected parts
Green house
Terras
Car port
Garden
Tuinhuis
Parking space

## Slide 9: They are interconnected …
… the urban fabric
Buildings as part of neighbourhoods and districts
Social housing
Paris urban fabric
UK
Beguinage (Leuven)
Beguinage

## Slide 10: Structure of the lecture
Buildings and the urban fabric
Modelling buildings as geospatial objects
Buildings in important European initiatives
The role of buildings in CCA & CCM
Conclusions

## Slide 11: Linking real world with digital world
… creating geospatial data models
ISO/TC 211
Geomatics
ISO 19100
Family of standards

## Slide 12: INSPIRE data specifications
… for 34 themes (including buildings)
The high level use cases for buildings

## Slide 13: INSPIRE data specifications
… detailed model
Including geospatial features, attributes
Horizontal
Geometry
Reference

## Slide 14: From 2D to 3D …
… Using footprints
Large-scale Basmap Flanders

## Slide 15: From 2D to 3D …
… also in INSPIRE
Using CityGML standard
(Open Geospatial Consortium)
Terrain intersection
(black line)

## Slide 16
Keyhole Markup
Language …

## Slide 17: From 2D to 3D …
… Towards Digital Twins
Example: Belmap- and Tygron platform
Simulating the impact on heat stress when implementing a new building (BIM)

## Slide 18
The impact of compensatory measures can be explored - e.g. planting trees

## Slide 19: Implementing new technologies …
… Combining CAD, GIS, Remote Sensing (RS)
The architectural world is used to CAD-tools, BIM as well.
This can be combined with geospatial and RS technologies …

## Slide 20: Structure of the lecture
Buildings and the urban fabric
Modelling buildings as geospatial objects
Buildings in important European initiatives
The role of buildings in CCA & CCM
Conclusions

## Slide 21: Buildings in European initiatives
… of course there are more
The already mentioned INSPIRE Directive was already mentioned
  Focuses on geospatial data sharing and interoperability
The Convenant of Majors
  Focuses on energy and climate actions at local level
The New Europena Bauhaus (NEB) initiative
  Focuses on transforming the built environment and lifestyles (citizens)
Built4People (B4P) projects and network
  Focusus on projects related to climate, energy and mobility

## Slide 22: Convenant of Majors
… plans, actions and community building
Reducing GHG emissions by 55% by 2030
Strengthening resilience
Alleviating energy poverty
Examples:
Cities Heat Detox
Cities Energy Savings Sprint

## Slide 23: Convenant of Majors
… plans, actions and community building
City Heat Detox

## Slide 24: New European Bauhaus
… Is also an architectural style / mouvement
sustainability, from climate goals to circularity, zero pollution, and biodiversity
aesthetics, quality of experience and style beyond functionality
inclusion, from valuing diversity to securing accessibility and affordability

## Slide 25
NEB Labs

## Slide 26: Built4People
… Part of Horizon Europe’s Cluster 5 (Climate, Energy and Mobility)

## Slide 27: Built4People
The METABUILDING platform is the digital meeting place for the innovation ecosystem of the European built environment sector.​​ It brings together stakeholders from the construction sector and emerging industrial sectors such as recycling & circular economy, additive manufacturing, nature-based solutions, and the digital industry.

## Slide 28: Structure of the lecture
Buildings and the urban fabric
Modelling buildings as geospatial objects
Buildings in important European initiatives
The role of buildings in CCA & CCM
Conclusions

## Slide 29: Role of buildings in CCA & CCM
… they can negatively or positively impact CC
In Belgium, 22% of CO2 is emitted by houses, 8% by other buildings
Dark colours
Paved gardens
Old walls
Non-isolated roofs
Paved squares
Old windows

## Slide 30: Role of buildings in CCA & CCM
… Example of Leuven 2030
Key Programmes
Renovate residential buildings
Renovate other buildings
Climate-neutral new buildings
A vibrant core and smart locations
Sustainable model shift
Greening vehicles
Green energy
Sustainable & healthy food
Greening (public) spaces
…

## Slide 31: Role of buildings in CCA & CCM
… Citizens can contribute, cities act & incentivize
Green roofs
Leuven
Green Roof: 500-7000€
Planting tree: 75€
Rain Garden: 350€
Water pit: 500€
Green buildings
Light colours
Unsealing soils
Isolating
Rain Garden

## Slide 32: Role of buildings in CCA & CCM
Greening of public space …
Nature-based
Solutions

## Slide 33
Current situation

## Slide 34
Small

## Slide 35
Medium

## Slide 36
Large

## Slide 37: Role of buildings in CCA & CCM
Supporting different ecosystem services
Water retention
Biodiversity
Pollination
Air quality
Cooling
CO2 storage
Food production
…
Tile Rockers in Flanders:
5.302.065 tiles broken

## Slide 38: Role of buildings in CCA & CCM
Gardens can play a major role
Citizens Science

## Slide 39: Structure of the lecture
Buildings and the urban fabric
Modelling buildings as geospatial objects
Buildings in important European initiatives
The role of buildings in CCA & CCM
Conclusions

## Slide 40: Some conclusions
Buildings are a key part of our built-up area, especially in an urban context
They are modelled and a key part of any Spatial Data Infrastructure (2D to 3D)
Several European initiatives support energy and CCA/CCM interventions, with a dedicated role for buildings
Buildings might contribute to CC, but also to its solutions